Fixing Bufferbloat on wireless
Or...
        Not every packet
        is sacred!
Dave Taht <dave.taht@bufferbloat.net>

---
Bufferbloat on ethernet is theoretically (mostly) fixed.
- Still needed:
  - BQL on more ethernet drivers (arm/mips anyone?)
  - Hardware Flow control support
  - Evolve fq_codel into PFIFO_Fast replacement
  - Deployment into devices where it counts most
- Ongoing work
  - Analysis/enhancement of fq_codel
  - More TCP and UDP work in the Linux 3.7+ stack

---
Bloat-fighting enhancements in Linux 3.6
- BQL (linux 3.3)
- FQ_CODEL (linux 3.5)
- TCP Small Queues (linux 3.6)
- Upcoming (post 3.6)
  - UDP small queues,
  - Host TCP RTT estimation in FQ_Codel
  - ?

---
Linux Ethernet Before BQL

---
PFIFO_FAST in Linux 3.6
on a BQL enabled driver

---
FQ_CODEL
on BQL enabled driver

---
ADSL modem w/FQ_Codel
with ethernet flow control
http://planet.ipfire.org/post/ipfire-2-13-tech-preview-fighting-bufferbloat

---
ADSL hw used above
Connection: ADSL2+ connection 16000/600 from Versatel (versatel.de) with
an average RTT of about 14ms.
Sphairon Turbolink AR860 which was the one
Versatel delivered to all their customers.
Test system was a Fujitsu-Siemens Futro S400:
AMD Geode 1000 MHz / 256 MB RAM / 4GB CF module for storage
Network Chipset: Realtek 8169

---
Bidirectional host throughput with TCP small queues – @100Mbit

---
- First attempt at BQL on smsc911x.
- Signed-off-by: Paul E. McKenney <paulmck@linux.vnet.ibm.com>
- diff --git a/drivers/net/ethernet/smsc/smsc911x.c b/drivers/net/ethernet/smsc/smsc911x.c
- index 62d1baf..16d6bfd 100644
- --- a/drivers/net/ethernet/smsc/smsc911x.c
- +++ b/drivers/net/ethernet/smsc/smsc911x.c
- @@ -1107,6 +1107,7 @@ static void smsc911x_tx_update_txcounters(struct net_device *dev)
- {
- struct smsc911x_data *pdata = netdev_priv(dev);
- unsigned int tx_stat;
- + unsigned int bytes_compl = 0, pkts_compl = 0;
- while ((tx_stat = smsc911x_tx_get_txstatus(pdata)) != 0) {
- if (unlikely(tx_stat & 0x80000000)) {
- @@ -1124,6 +1125,8 @@ static void smsc911x_tx_update_txcounters(struct net_device *dev)
- } else {
- dev->stats.tx_packets++;
- dev->stats.tx_bytes += (tx_stat >> 16);
- + pkts_compl++;
- + bytes_compl += (tx_stat >> 16);
- }
- if (unlikely(tx_stat & TX_STS_EXCESS_COL_)) {
- dev->stats.collisions += 16;
- @@ -1140,6 +1143,7 @@ static void smsc911x_tx_update_txcounters(struct net_device *dev)
- }
- }
- }
- + netdev_completed_queue(dev, pkts_compl, bytes_compl);
- }
- /* Increments the Rx error counters */
- @@ -1607,6 +1611,7 @@ static int smsc911x_stop(struct net_device *dev)
- /* At this point all Rx and Tx activity is stopped */
- dev->stats.rx_dropped += smsc911x_reg_read(pdata, RX_DROP);
- smsc911x_tx_update_txcounters(dev);
- + netdev_reset_queue(dev);
- /* Bring the PHY down */
- if (pdata->phy_dev)
- @@ -1650,6 +1655,7 @@ static int smsc911x_hard_start_xmit(struct sk_buff *skb, struct net_device *dev)
- wrsz >>= 2;
- pdata->ops->tx_writefifo(pdata, (unsigned int *)bufp, wrsz);
- + netdev_sent_queue(dev, skb->len);
- freespace -= (skb->len + 32);
- skb_tx_timestamp(skb);
- dev_kfree_skb(skb);
ADDING
BQL
To
Ethernet
IS
EASY

---
Other ongoing debloating work
- Stephen Hemminger is adding BQL support to various virtualized network drivers
- John Crispin is working on two ADSL modems
- Felix Feitkau hacking on ath9k
- CeroWrt project expanding to new devices
- Google team is fixing stuff all through the stack (mostly targetted at ethernet), Andrew Mcgregor joining google in January
- Codel and fq_codel in the lab at a very large cable ISP and cablelabs
- Multiple companies looking at the core techniques on LTE, 3g, VPON, and cable head-ends
- And then... there's wifi on home routers...

---
 Fixing bufferbloat on wireless has a long way to go...

---
The state of wifi is dismal...
(linuxcon network, monday)

---
TCP's behavior (TCP 101)
TCP will always fill the biggest buffer on the path
The retries and retransmits inherent in wifi increase the RTT time, which fools TCP into growing its window. The more buffering, the bigger the spikes, and the bigger the collapses and resulting transmits, resulting in a loss of real bandwidth.
This is a ns2 model from:
http://staff.science.uva.nl/~delaat/netbuf/bufferbloat_BG-DD.pdf
(.5Mbit uplink)

---
Some buffering is needed...
but any extra buffering just adds latency.

---
Experiments in Wifi
(the yurtlab)
Campground in california with varying terrain and clear signals
- 10 station wireless mesh network built on ath9k based hardware.
- No competing wifi signals

---
BQL won't work on wireless-n
- Bandwidth is too dynamic
- Bound by TXOPs
- Per station queues vary in ideal size (802.11g, 802.11n, 802.11ac)
- But some of the principles apply:
  - Track a skb from creation to completion and actual exit from the hw.
  - Try to keep as little data in the driver as possible
- It would be nice, regardless of this talks focus on wifi, to get more BQL enabled ethernet drivers. (nag, nag, nag).
- This will help demonstrate the benefits to applying similar techniques to wifi.

---
Wireless-n latency under load
FQ_codel helps on a voip-like load... but...
Device buffers on wireless are a huge problem.
With a rate change to 1Mbit, the whitespace (delay) below the red bar grows by 100X!

---
Fiddling with driver buffering on ath9k
- Out of tree ath9k patch (openwrt only)
- cat /sys/kernel/debug/ieee80211/phy0/ath9k/qlen_{be,vo,bk,vi}
- Changing these to minimal values is “interesting”, in viewing how txops interact with actual traffic...
- And the net result of applying the existing FQ_codel on top of minimum aggregation, today, is good,
- conversely, maximum aggregation has terrible effects on latency, presently:

---
Experiments on ath9k at MCS4 –Aggregate buffering leads to 50% more bandwidth
in exchange for 10x more latency.
- qlen 100, nttcp -t: 5.966/57.104/192.017/26.674 ms; 52.2376 Mbps
- qlen 35, nttcp -t: 15.636/54.823/108.921/19.762 ms; 52.4675 Mbps
- qlen 12, nttcp -t: 4.768/29.439/132.924/27.159 ms; 51.2619 Mbps
  qlen 4, nttcp -t: 2.631/20.500/152.741/31.549 ms; 40.3949 Mbps
- qlen def, ntccp -t: 2.010/21.851/317.085/49.323 ms; 35.8268 Mbps
- qlen 100, nttcp -r: 23.225/44.101/142.835/21.181 ms; 36.6789 Mbps
- qlen 35, nttcp -r: 3.755/23.413/ 83.530/15.329 ms; 35.4602 Mbps
- qlen 12, nttcp -r: 4.318/10.251/ 96.773/12.008 ms; 31.1557 Mbps
- qlen 4, nttcp -r: 2.733/ 4.507/ 16.353/ 1.917 ms; 24.6688 Mbps
- qlen def, nttcp -r: 2.119/ 4.999/ 64.968/ 7.275 ms; 27.3645 Mbps
- https://lists.bufferbloat.net/pipermail/cerowrt-devel/2012-August/000458.html

---
What's needed to fix wifi
- Tight control loops
- Minimal queues and outstanding packets
- Per Station Fair Queuing
- Auto-adjusting buffer sizes based on apparent delay (codel)
- Feedback at every level up the stack

---
Bandwidth/latency tradeoff in wireless-n
- 1) Wireless-n does packet aggregation to gain bandwidth. FQ on an AP splits up streams into often non-aggregatable chunks because it doesn't have per station destination information. Mac nexthop doesn't help on bridging...
- 2) Reducing the hw queue length has a negative effect on throughput over-all in the current driver design
- 3) TXOPs, not bytes are the limiting factor
- 4) You need a queue as a shock absorber, but you don't need 4 queues to manage the hw queues, one queue that can feed 4 queues would be better and save on memory use besides. Multiple SSIDs also lead to excessive buffering in the present architecture.

---
Proposed Wireless fixes
- Improve Testing tools to reflect real-world cases
- Tie the codel aqm and minstrel's rate algorithms together better
- Add per station queues to the wifi stack (mfq_codel? Mac80211?)
- Move codel into the mac80211 layer and make it's maxtarget value account for the number of active stations and their aggregate queue lengths
- Fair queue inside each station queue
- Come up with additional sane drop strategies within aggregates
- Address the hidden management frames problem
- Come up with a way to fund and test the work

---
The RRUL benchmark
Realtime Response Under Load
- Loads up a network with 8 bidirectional streams
- Tests web/voip performance unloaded and loaded
- Also tests classification
- Tests IPv6
- Available via:
  https://lists.bufferbloat.net/pipermail/bloat/2012-November/001113.html

---
Partial RRUL after hours at linuxcon

---
FQ_Codel Principles
- HEAD DROP, not tail drop.
- Queues are shock absorbers
- What matters is the delay within a flow.
- Shoots packets in elephant flows after they start accumulating delay. Don't shoot anything else!
- See Van Jacobson's preso at: http://recordings.conf.meetecho.com/Recordings/watch.jsp?recording=IETF84_TSVAREA&chapter=part_3
- Or Eric Dumazet's preso at: http://linuxplumbers.ubicast.tv/videos/codel-and-fq_codel-fighting-the-delays/

---
Dynamic Link: the fun stuff
- Nominal 100 Mbps link with rate changes, buffer size of 830 packets
- 4 FTPs, 5 packmime connections/sec
- Note the throughput line for undersized buffer of 10 packets: throughput is about 75% less. CoDel same throughput as tail drop but 2.7ms median delay, 5ms 75th percentile

---
CoDel in a nutshell
- CoDel assumes that a standing queue of target is acceptable (as determined by the local minimum) and that it is unacceptable to drop when there are fewer than an MTU worth of bytes in the buffer
- To ensure that the minimum value is not stale, it has to have been experienced in the most recent interval (sliding window)
- When the sojourn time has exceeded target for at least an interval, a packet is dropped and a control law used to set the next drop time
- The next drop time is decreased in inverse proportion of the square root of the number of drops since the dropping state was entered (to get a linear change in throughput)
- When the sojourn time goes below target the controller stops dropping.

---
Codel overview, continued
Prevented from re-entering dropping state too soon after exiting it and resumes the dropping state at a recent control level if one exists
Target and interval are constants: acceptable queue delay and a time on the order of a worst case RTT of connections through the bottleneck. Experimentally determined target as 5ms and interval of 100ms works well for range of RTTs from 10ms to 1sec, with excellent performance in 10ms - 300ms range.

---
CoDel Can’t Fix Concatenated Queues
Solutions:
  - rate control
  - AQM in CM
  - Flow control
Flow control

---
Bandwidth is not a constant
It might be 300Mbit one ms
Bandwidth is Not a Constant
It might be 100 Mbit
… for several ms
[Speaker Notes: A normal TCP stream looks like this Btw, this is packet aggregation at work -]

---
Delays of 0 Mbit for 100s of ms!

---
300 Mbit for an instant – with wireless-N aggregation, wedging as many packets into the backlog as possible...

---
Better Leveraging Minstrel Statistics
- The only time I ever see MCS 15 is when the AP is a few feet away from the AP.
- There are many ideas buried deep within minstrel that would be good to evaluate and provide a better API to.
- NS3 emulation is good, wireless-n and ac, not so much

---
- root@davesroof:/sys/kernel/debug/ieee80211/phy0/netdev:wlan0/stations/00:27:22:a8:a3:1a# cat rc_stats
- type rate throughput ewma prob this prob this succ/attempt success attempts
- HT20/LGI MCS0 3.6 58.0 100.0 0( 0) 306 384
- HT20/LGI MCS1 8.8 75.4 19.9 0( 0) 731 1185
- HT20/LGI MCS2 5.1 31.0 0.0 0( 0) 1578 2538
- HT20/LGI t MCS3 14.4 69.2 100.0 0( 0) 21405 26086
- HT20/LGI T PMCS4 27.4 97.6 100.0 0( 0) 153050 185927
- HT20/LGI MCS5 14.0 41.4 0.0 0( 0) 1827 4486
- HT20/LGI MCS6 0.0 0.0 0.0 0( 0) 10 1426
- HT20/LGI MCS7 0.0 0.0 0.0 0( 0) 0 1428
- HT20/LGI MCS8 8.4 71.5 100.0 0( 0) 528 784
- HT20/LGI MCS9 5.3 25.7 0.0 0( 0) 9196 12302
- HT20/LGI MCS10 10.4 37.1 0.0 0( 0) 18929 28297
- HT20/LGI MCS11 14.1 41.7 100.0 0( 0) 23875 35908
- HT20/LGI MCS12 0.0 0.0 0.0 0( 0) 591 2410
- HT20/LGI MCS13 0.0 0.0 0.0 0( 0) 0 1428
- HT20/LGI MCS14 0.0 0.0 0.0 0( 0) 0 1433
- HT20/LGI MCS15 0.0 0.0 0.0 0( 0) 0 1431
- Total packet count:: ideal 217212 lookaround 14954
- Average A-MPDU length: 1.0

---
Some useful ath9k stats
    root@davesroof:/sys/kernel/debug/ieee80211/phy0/ath9k# cat xmit
    Num-Tx-Queues: 10 tx-queues-setup: 0x10f poll-work-seen: 36206
        BE BK VI VO
    MPDUs Queued: 27436 174 15066 12730
    MPDUs Completed: 27322 174 15062 12708
    MPDUs XRetried: 114 0 4 22
    Aggregates: 94194 5 0 0
    AMPDUs Queued HW: 620975 49 21536 0
    AMPDUs Queued SW: 438841 7 0 0
    AMPDUs Completed: 1045702 34 6476 0
    AMPDUs Retried: 438217 728 413300 0
    AMPDUs XRetried: 14114 22 15059 0
    FIFO Underrun: 0 0 0 0
    TXOP Exceeded: 0 0 0 0
    TXTIMER Expiry: 0 0 0 0
    DESC CFG Error: 0 0 0 0
    DATA Underrun: 0 0 0 0
    DELIM Underrun: 0 0 0 0
    TX-Pkts-All: 1087252 230 36601 12730
    TX-Bytes-All: 712792668 12570 3244394 1330716

---
Bufferbloat Canonical reference
- ACM Queue: “Bufferbloat”
  – Jim Gettys, Kathie Nichols
  http://queue.acm.org/detail.cfm?id=2071893
- ACM Queue – “What's wrong with the Internet?” Vint Cerf, Van Jacobson, Jim Gettys, Nick Weaver
  http://queue.acm.org/detail.cfm?id=2076798
- Jim Gettys' Google Video
- Bufferbloat Project: http://bufferbloat.net

---
CeroWrt... What if home routers... ...didn't suck?
And the software was 100% open source?
- Measuring BW to
  Various points
- Testing DNS
- Measuring user habits
- Measuring Provided Bandwidth and Shapers
- We're Fixing Drivers
- Validating the Linux stack
- Doing End To End testing
- Analyzing Wireless
- Fixing Bufferbloat!
- Implementing Ipv6, DNSsec, and mesh networking
- Implementing RFCs

---
Future Directions
- Start working on Android
- Find chipsets that can be made to work better
- Create more proof of principle devices
- Drive adoption into new hardware
- Influence design of new hardware

---
What if you could save 100m people 10 seconds of waiting on wifi... a day?
1,000,000,000 seconds/(3600 secs in an hour, 8 hours a day) = 34,722 work days of productivity lost, currently, waiting on wifi...

---
Questions?
 Bufferbloat.net Resources
Bufferbloat.net: http://bufferbloat.net
Email Lists: http://lists.bufferbloat.net
IRC Channel: #bufferbloat on chat.freenode.net
CeroWrt: http://www.bufferbloat.net/projects/cerowrt
Other talks: http://mirrors.bufferbloat.net/Talks
    Jim Gettys Blog – http://gettys.wordpress.com
    Dave Täht's Blog – http://nex-6.taht.net
    Use Google scholar for bufferbloat.
Help out where you can! Resources, rackspace, money, developers, money, theorists, & awareness, are all needed... as...
        We're all in this bloat together.